## Slide 1: All About Lights Lesson 3
Notes: Overview: In this lesson, students will review the learned programming scripts associated with common input devices including the keyboard and the mouse. Building on this previous experience, students will be introduced to the use of Events scripts. Students will also explore new input and output devices about lights – light sensors and LED bulbs and display panels – to expand their understanding of the I/O System.
Image Source: https://pixabay.com/vectors/rainbow-colors-electronic-diodes-26389/

## Slide 2: Tasks in this lesson
Recall the Input function
Understand the Output function
Explore the use of Light Sensor
Notes: Show Slide 2 to inform the class about the agenda and task in this lesson.

## Slide 3: Warm Up
Notes: This phase aims to help review what has been learned in the previous lesson quickly. Pay attention to the triggering devices associated with the chatbot project.

## Slide 4: Your Chat Bot Project
How did you make the bot talk? (Tip: The speech/thought bubble)
What kind of script did you use to develop the interactive chatting effect?
Notes: Have students recall and reflect upon their chatbot projects completed in the previous lesson.
  Let students talk about the programming scripts they used to make the bot “say” or display something through the speech or thought bubble.
Ask students to share how they made the bot “smart” to understand and respond to human words.

## Slide 5: Phase 1
Notes: In this phase, students will summarize the programming scripts associated with input information from the keyboard and the mouse. Students will be introduced to Events scripts associated with a triggering input device.

## Slide 6: Task 1 The Inputs You Know
How many input programming scripts have you learnt?
What are the inputs from when you execute the scripts?
Notes: Show Slide 6 to have students reflect upon their chatbot project development experience.
  How many input programming scripts have you learned?
  What are the inputs from when you execute the scripts?
Instruct students to complete Task 3-1 to circle the correct input device for the programming script.
  Remind the class that they can drag the corresponding scripts in mBlock to have a try. Think about the device used when executing the script.

## Slide 7
Notes: Show Slide 6 to have students reflect upon their chatbot project development experience.
  How many input programming scripts have you learned?
  What are the inputs from when you execute the scripts?
Instruct students to complete Task 3-1 to circle the correct input device for the programming script.
  Remind the class that they can drag the corresponding scripts in mBlock to have a try. Think about the device used when executing the script.
Image Source: https://pixabay.com/vectors/mouse-electronics-keyboard-computer-1412284/

## Slide 8: Events
An event is an action that can cause things to happen.
Notes: Introduce the meaning of the Events script with the example of turning on the light.

## Slide 9: Events
The action of pressing the button is an “Event”.
Notes: Introduce the meaning of the Events script with the example of turning on the light.

## Slide 10: Events
Press a button to turn on the light
Click on the Green Flag or a sprite
Press the space key on the keyboard
Notes: Ask students to discuss any real-life example they know that can explain the concept of the event.
  Ask students to first think of the situation;
  Then, have students identify and figure out what the triggering device is in the situation.
  Ask students to consider what the triggering device does? Act as a button? Collect any information from the outside? Adjust the degree of something?

## Slide 11: Events Blocks
Notes: Point out the triggering device during using mBlock: the keyboard and the mouse.
  While displaying the Events scripts, remind that there is one Events script that is associated with mBot. It can be used when it is in the “Upload” mode, which means you want to upload a program into mBot, rather than program the sprite in the mBlock platform.

## Slide 12: Phase 2
Notes: In this phase, students will create their first code for mBot in mBlock. Students need to figure out there are two modes while programming mBot: The Upload Mode and the Live Mode.

## Slide 13: Events Blocks for mBot
Notes: Instruct students to open the mBlock application and find the “Mode Switch” in the information box at the bottom of the Stage Area.
  Ask students to click on different buttons associated with the mode, and parallelly, open the panel of the Events category in the Blocks Area. Have them observe the difference that appeared when changing the mode.
  Briefly explain the use of the two different modes:
  In the Upload mode, you need to upload the compiled program to the device. After being successfully uploaded, the program can still run properly on the device no matter whether the device is connected to the computer or not.
  In the Live mode, you can view the program execution effect in real time, which facilitates the commissioning of the program. In addition, you can implement the interaction between devices and sprites by using the broadcast and variable blocks.
  For more information, please refer to the online tutorial available from: https://www.mblock.cc/doc/en/hardware-basic/mode.html.

## Slide 14: Events Scripts for mBot
Any difference?
How to switch the two panels?
Notes: Instruct students to open the mBlock application and find the “Mode Switch” in the information box at the bottom of the Stage Area.
  Ask students to click on different buttons associated with the mode, and parallelly, open the panel of the Events category in the Blocks Area. Have them observe the difference that appeared when changing the mode.
  Briefly explain the use of the two different modes:
  In the Upload mode, you need to upload the compiled program to the device. After being successfully uploaded, the program can still run properly on the device no matter whether the device is connected to the computer or not.
  In the Live mode, you can view the program execution effect in real time, which facilitates the commissioning of the program. In addition, you can implement the interaction between devices and sprites by using the broadcast and variable blocks.
  For more information, please refer to the online tutorial available from: https://www.mblock.cc/doc/en/hardware-basic/mode.html.

## Slide 15
Notes: Instruct students to open the mBlock application and find the “Mode Switch” in the information box at the bottom of the Stage Area.
  Ask students to click on different buttons associated with the mode, and parallelly, open the panel of the Events category in the Blocks Area. Have them observe the difference that appeared when changing the mode.
  Briefly explain the use of the two different modes:
  In the Upload mode, you need to upload the compiled program to the device. After being successfully uploaded, the program can still run properly on the device no matter whether the device is connected to the computer or not.
  In the Live mode, you can view the program execution effect in real time, which facilitates the commissioning of the program. In addition, you can implement the interaction between devices and sprites by using the broadcast and variable blocks.
  For more information, please refer to the online tutorial available from: https://www.mblock.cc/doc/en/hardware-basic/mode.html.

## Slide 16: Task 2 Upload the Program
Model and upload the demo program below into your mBot:
Notes: Instruct students to complete Task 3-2 in the activity sheet.
  Can two to four students share a mBot.
  Have students assemble the LED panel onto mBot and connect it to the computer. Remind them to pay attention to the number of the occupied mBot’s port (Port 1 to 4).
  Select the “Upload” mode in mBlock and click on the “Connect” button.
  Model the demo program to create one in mBlokc and then upload the program to the mBot.

## Slide 17: Task 2 Upload the Program
Add the LED panel
Notes: Instruct students to complete Task 3-2 in the activity sheet.
  Can two to four students share a mBot.
  Have students assemble the LED panel onto mBot and connect it to the computer. Remind them to pay attention to the number of the occupied mBot’s port (Port 1 to 4).
  Select the “Upload” mode in mBlock and click on the “Connect” button.
  Model the demo program to create one in mBlokc and then upload the program to the mBot.

## Slide 18: Task 2 Upload the Program
Choose the Upload mode
Notes: Instruct students to complete Task 3-2 in the activity sheet.
  Can two to four students share a mBot.
  Have students assemble the LED panel onto mBot and connect it to the computer. Remind them to pay attention to the number of the occupied mBot’s port (Port 1 to 4).
  Select the “Upload” mode in mBlock and click on the “Connect” button.
  Model the demo program to create one in mBlokc and then upload the program to the mBot.

## Slide 19
Find and construct the scripts below:
Events
Control
Sensing
Show
Notes: Show the Slide 19 to present the four scripts needed in this exercise.
  At this stage, it is not necessary to explain the function of each script in detail.
  When executing the program, students can add a “wait 1 second(s)” script following the Show script within the “forever” control structure, if they find the displayed number changed too fast to be observed.

## Slide 20
Check the port you connect:
Here hides a Light Sensor. It can help mBot “feel” the brightness.
Should be the same port
Notes: Remind students that when using the Show script, remember to select the correct port in the block. Also, remind that they should choose the “show number” block.
Let students execute the program with their partners. Encourage them to try different means to change the brightness condition around mBot.
  They can record the data they read in either the activity sheet or a form made by themselves.

## Slide 21: Task 2 Upload the Program
Question: Point out the Input and Output in this demo
Light Sensor
mBlock
LED Panel
Notes: Have students report the means they used to affect the light sensor and the change of the data. Also, ask the class to point out the input device and output device functioned in this experiment.

## Slide 22: Practice
Notes: This phase will introduce a new electronic device as a bonus for programming practice. Students can either program the two LED bulbs or explore other LED animation effects by using Show scripts.

## Slide 23: Task 3 Light up mBot
Use different Events Scripts to trigger the LEDs on mCore:
Choose the Live mode in mBlock
Notes: Briefly introduce the LED bulbs in mBot as well as the associated LightSound scripts.
Instruct students to choose one light effect project pathway to practice.
  One pathway is to program the light effect by means of the two LED bulbs in the mBot main control board. For example, press different number key to trigger different colors of lights.
  Another pathway is to continue to explore the light animation through the LED panel. They can doodle or write something and displayed it on the LED matrix.

## Slide 24: Wrap Up

## Slide 25
Keywords
Output Device
LED Blubs
Light Sensor
Notes: Show Slide 25 to point out the key points of this lesson.

## Slide 26: Clean Up