## Slide 1: mBot the Musician Lesson 11
Notes: Overview: Lesson 11 will revisit the composition play, however, via using different programming scripts and algorithms. First, students need to explore how to utilize the “light sensor” Sensing block as a condition in the conditional algorithm. Students can control and compare different kinds of methods that affect the brightness situations around the light sensor of mBot. Building on this experiment and the collected data, students will then explore how to use the values of light intensity in the conditional algorithms to play different notes.

## Slide 2: Tasks in this lesson
Use conditional algorithms to trigger different (or multiple) interactive effects
Understand that broadcasting is a way to make the hardware and the software interplay
Notes: Show Slide 2 to inform the class about the agenda and task in this lesson.

## Slide 3: Warm Up
Notes: This phase begins with brainstorming about how to make “music” without musical instruments. Students need to associate with their real-life experience to propose possible ways of creating sound effects and then explore how to transfer to creating a musical computing artifact in the next phase.

## Slide 4: Task 1 Making Music with …
Discussion:
Except instrument, we can also make “music” through…
Notes: Show Slide 4 to pose the question to the class and have them discuss:
  Except for musical instruments, could you make “music” (or pleasure sounds) by using everyday objects (i.e. other kinds of physical methods)?
  Play a video clip that people use cups to make music. Display the example to spark the thought and encourage students to brainstorm possible ideas.
Indicate that mBot can use its light sensor to make music. Have students recall what they have learned in Lesson 3 before going to the next phase.
Image Source: https://pixabay.com/illustrations/liquid-water-clean-clean-water-cup-1210614/
https://pixabay.com/illustrations/box-cardboard-cardboard-box-package-1536798/
https://pixabay.com/illustrations/applause-hands-clap-clapping-black-4342965/

## Slide 5: Example: Musical Cup
A video clip of this example is available from:
https://youtu.be/dM6vnN4pXygg
Notes: Show Slide 4 to pose the question to the class and have them discuss:
  Except for musical instruments, could you make “music” (or pleasure sounds) by using everyday objects (i.e. other kinds of physical methods)?
  Play a video clip that people use cups to make music. Display the example to spark the thought and encourage students to brainstorm possible ideas.
  In Slide 5 there is the example of making music with cups. Due to the copyright, the slideshow cannot provide the video clip. However, a recommended source is indicated in this slide which is available from:
https://youtu.be/dM6vnN4pXygg.
Indicate that mBot can use its light sensor to make music. Have students recall what they have learned in Lesson 3 before going to the next phase.

## Slide 6: Phase 1
Notes: This phase aims to introduce the use of logical operators in association with conditional constructs. Students will explore how to use Operators blocks to create and set up more conditions – in particular, when they need to create more than two pathways based on the input from a single sensor or any other kind of input device and electronics.

## Slide 7: Task 2 Light and Sound
How to use the brightness of the environment as a condition in an algorithm
Could this block place inside the condition elongated hexagonal space?
Notes: Show Slide 7 and ask students to model the situation shown in the slide in mBlock.
  Ask students to drag the “if…, then…” Control block and the “light sensor” block, try whether they could place the “light sensor” block inside the “if…, then…” Control block’s condition.
  Have students go back to the Block Area in mBlock and figure out what kinds of shapes of the blocks may be able to combine the “light sensor” block and the “if…, then…” block.
  Remind students that pay careful attention to the shape of the block.
  Also, indicate that they could go to the “Operators” category first. This category is relatively new and not explained specifically during the previous lessons.
Ask students to report their findings and try to predict the possible functions of the script.

## Slide 8: Logical Operator
An operator is a number value that can be added to a conditional or any block you can type in to change the outcome
Notes: Show Slide 8 to explain the meaning of logical operators.

## Slide 9: Logical Operator
Use Operators blocks as a medium
… is less than …
… is greater than …
… is equal to …
Notes: Show Slide 9 to display the three kinds of common Operators blocks that can perform math functions.
  Indicate these three blocks can compare the value of the brightness input from mBot’s light sensor with another set-up number.
Show Slide 10 to give some examples that combine the “light sensor” block and an Operator block.
  Display two kinds of examples: one is if the value of the brightness is less than 90, and the other is the value of the brightness is greater than 900.

## Slide 10: Logical Operator
Use the LED panel to collect brightness data
Define the range in the Operators blocks, e.g.:
Notes: Show Slide 9 to display the three kinds of common Operators blocks that can perform math functions.
  Indicate these three blocks can compare the value of the brightness input from mBot’s light sensor with another set-up number.
Show Slide 10 to give some examples that combine the “light sensor” block and an Operator block.
  Display two kinds of examples: one is if the value of the brightness is less than 90, and the other is the value of the brightness is greater than 900.

## Slide 11: AND Operators Block
What if we want to define a range between “90” and “300”? How could we combine the two scripts shown below?
Notes: Ask students to think of what if they want to set up a third script ranged between 90 and 900, what kind of block could help.
  Show Slide 11 to introduce using the “… and …” Operators block as a possible solution to the above question.
  Show Slide 12 to demonstrate the example of the use of “… and …” Operators.

## Slide 12: AND Operators Block
The can join the two together
(90 < < 300)
Notes: Ask students to think of what if they want to set up a third script ranged between 90 and 900, what kind of block could help.
  Show Slide 11 to introduce using the “… and …” Operators block as a possible solution to the above question.
  Show Slide 12 to demonstrate the example of the use of “… and …” Operators.

## Slide 13: Phase 2
Notes: This phase will focus on the combination of logical operators and conditional constructs in the case of the use of nested conditional algorithms. Students will compare the two kinds of conditional algorithms in certain depth – the parallel “if…, then…” and the nested “if…, then…; else…”.
However, it is not necessary for students to differentiate the actual logical difference between the two kinds of constructs in this lesson.

## Slide 14: Conditionals and Operators
How to construct the conditional algorithm with Operators blocks?
Notes: Instruct students to add the “if…, then…” conditional constructs and create the conditional constructs shown in Slide 14.

## Slide 15
What’s different?
Notes: Ask students to think of how to combine the three conditional scripts together to make an executable program.
  In this stage, students only need to experiment by defining three pathways in this phase.
  Instruct students to decide the content of “Action 1”, “Action 2”, and “Action 3” – for example, make mBot’s LED panel display different patterns or words; make the buzzer play different sound effects, etc.
Show Slide 15 and 16 to ask students to discuss whether the two example constructs are different from each other or not?
  Instruct students to model the demo programs in the slideshow and run them. Also, remind them that they can discuss from the perspective that which one is readable for them.
  If you want to challenge students, ask them to consider the four- or eight-pathway conditional constructs.
  Please note that the different format may lead to the same result; however, if associated with what makes an algorithm easy-to-read and well-defined, the latter example can make the code simple in the case of three-pathway conditional constructs.

## Slide 16
What’s different?
Notes: Ask students to think of how to combine the three conditional scripts together to make an executable program.
  In this stage, students only need to experiment by defining three pathways in this phase.
  Instruct students to decide the content of “Action 1”, “Action 2”, and “Action 3” – for example, make mBot’s LED panel display different patterns or words; make the buzzer play different sound effects, etc.
Show Slide 15 and 16 to ask students to discuss whether the two example constructs are different from each other or not?
  Instruct students to model the demo programs in the slideshow and run them. Also, remind them that they can discuss from the perspective that which one is readable for them.
  If you want to challenge students, ask them to consider the four- or eight-pathway conditional constructs.
  Please note that the different format may lead to the same result; however, if associated with what makes an algorithm easy-to-read and well-defined, the latter example can make the code simple in the case of three-pathway conditional constructs.

## Slide 17: Conditionals and Operators
Predict the two example algorithms
Model and run in mBlock
Modify and change the value in the condition
Notes: Ask students to think of how to combine the three conditional scripts together to make an executable program.
  In this stage, students only need to experiment by defining three pathways in this phase.
  Instruct students to decide the content of “Action 1”, “Action 2”, and “Action 3” – for example, make mBot’s LED panel display different patterns or words; make the buzzer play different sound effects, etc.
Show Slide 15 and 16 to ask students to discuss whether the two example constructs are different from each other or not?
  Instruct students to model the demo programs in the slideshow and run them. Also, remind them that they can discuss from the perspective that which one is readable for them.
  If you want to challenge students, ask them to consider the four- or eight-pathway conditional constructs.
  Please note that the different format may lead to the same result; however, if associated with what makes an algorithm easy-to-read and well-defined, the latter example can make the code simple in the case of three-pathway conditional constructs.

## Slide 18: Practice
Notes: Building on their previous experiment and findings, students will use conditional algorithms to create a “Light Piano”, which means the notes are generated due to different kinds of brightness circumstances.

## Slide 19: Task 3 Light Piano
Could the brightness of environment trigger the playing of C Major Notes?
Notes: Inform the class about the “Light Piano” they will create in this phase.
  Show Slides 19 and 20 to help recall the music fundamentals learned in Lesson 7.
  In this case, students only need to generate sound effects within the scale of C Major. For advanced students who have sufficient musical knowledge, encourage them to challenge themselves and help instruct their peers when someone needs help.
Image Source: https://pixabay.com/vectors/keyboard-piano-instrument-music-25702/

## Slide 20
C Major:
Do
Re
Mi
Fa
Sol
La
Ti
Do
C4
D4
E4
F4
G4
A4
B4
C5
Notes: Inform the class about the “Light Piano” they will create in this phase.
  Show Slides 19 and 20 to help recall the music fundamentals learned in Lesson 7.
  In this case, students only need to generate sound effects within the scale of C Major. For advanced students who have sufficient musical knowledge, encourage them to challenge themselves and help instruct their peers when someone needs help.

## Slide 21: Task 3 Light Piano
Use the range of light intensity to try to play the C Major, for example:
Notes: Instruct students to create and test the “Light Piano” by using conditional algorithms with logical operators.
  Remind students that they can refer to the brightness data they have recorded at the beginning of this lesson. Set up no more than eight scales for note-playing.
  Students can choose what kind of conditional algorithms they want to employ.

## Slide 22
Notes: Instruct students to create and test the “Light Piano” by using conditional algorithms with logical operators.
  Remind students that they can refer to the brightness data they have recorded at the beginning of this lesson. Set up no more than eight scales for note-playing.
  Students can choose what kind of conditional algorithms they want to employ.

## Slide 23: Task 3 Light Piano
Think:
How should you construct the conditional algorithm in the project?
Notes: Encourage students to try and test to modify the light intensity conditions set in the conditional construct. Ask them to consider the following question during the experiment:
  How should you construct the conditional algorithm in the project?
  Why should we use the Forever block?
  Is it easy for mBot to play the notes?

## Slide 24: Task 3 Light Piano
Think:
Why should we use the Forever block?
Is it easy for mBot to play the notes?
Notes: Encourage students to try and test to modify the light intensity conditions set in the conditional construct. Ask them to consider the following question during the experiment:
  How should you construct the conditional algorithm in the project?
  Why should we use the Forever block?
  Is it easy for mBot to play the notes?

## Slide 25: Wrap Up

## Slide 26: Key Concept
Operators blocks can perform math functions to set up conditions
Pay attention to when and how to combine loops and conditionals in a computing artifact
Notes: Instruct students to reflect on how the key concepts are embodied in the project. Importantly, ask students to elaborate on their experience of combining looping and conditional constructs.

## Slide 27: Clean Up